Water Utility O&M Activities

Unplanned Potable Water Discharge to Storm Drain

Best Management Practices (BMPs)

San Francisco Bay Municipal Regional Stormwater NPDES Permit (MRP) Provision C.15.b.iii. (2)

General Best Management Practices (BMPs)

- Unplanned discharges are non-routine activities such as water line breaks, leaks, overflows, fire hydrant shearing and emergency flushing.

- Record response times. (see Field Forms)

- Contain the discharge and attain safety of the discharge site.

- Dechlorinate potable water. Example types of dechlorination equipment available:

- Dechlor mat (3’ x 4’) used with tablets

- Dechlor strip (6” x 36”) used with tablets

- Diffuser used with tablets (can be used during repair operations)

- Drip system used with liquid

- Dechlor tablets in flowpath (e.g. in gutter or before stormdrain)

- Place erosion and sediment control devices in flow path if needed. Erosion and sediment control:

- Slows the flow of water, preventing erosion and/or allowing some portion of the sediment to settle out and/or;

- Protects bare earth surfaces to preclude the detachment of soil particles from the flow of water;

- Bypasses sediment using piping to move flow around potential pollutants;

- Prevents the flow of water from reaching or picking up sediment by using berms or dikes.

- Monitor release after BMPs and before discharge to storm drain for chlorine residual, turbidity and pH, if possible.

- Record results. (see Field Form)

- Close operation.

  - Inspect the flow path for erosion damage or sediment deposition

  - Cleanup and dispose of control materials appropriately

- Notify Regional Water Board staff within 24 hours by phone/e-mail if discharge > 50,000 gallons and chlorine residual > 0.05 mgl/L.

- Notify state Office of Emergency Services within 2 hours of becoming aware of:

1)	aquatic impacts (e.g. fish kill)

2)	when discharge might endanger or compromise public health and safety

Resources:

Guidelines for the Development of Your Best Management Practices (BMP) Manual for Drinking Water System Releases, CA-NV American Water Works Association, 2005. http://ca-nv-awwa.org/iMISpublic/AM/Template.cfm?Section=Resource_Center34&Template=/CM/ContentDisplay.cfm&ContentID=7742

SCVURPPP Water Utility Operation and Maintenance Discharge Model Pollution Prevention Plan approved January 20, 2011. http://www.scvurppp-w2k.com/pdfs/1011/WUDPPP_01_20_11.pdf

City of Palo Alto Water Utility Operation and Maintenance Discharge Model Pollution Prevention Plan (EOA August 22, 2011)

# Text boxes

Filter bag w/dechlor tablets in gutter (Palo Alto WUDPPP)

Example erosion and sediment controls: filter bag over sump pump hose discharge, storm drain inlet protection, flow path check filters, vegetation filtration, flow diversion (surface protection), armoring (surface protection), diffuser.

Example erosion and sediment controls: filter bag over sump pump hose discharge, storm drain inlet protection, flow path check filters, vegetation filtration, flow diversion (surface protection), armoring (surface protection), diffuser.

dechlor mat from Pollardwater.com

filtration, flow diversion (surface protection), armoring (surface protection), diffuser.

Benchmarks

Chlorine residual: <0.05 mg/L

pH: >6.5 or <8.5

Turbidity: Low

Final Draft  September 2012

SMCWPPP Water Utility Work Group Fact Sheet #3

Unplanned Potable Water Discharge to Storm Drain BMPs

Example erosion and sediment controls: filter bag over sump pump hose discharge, storm drain inlet protection, flow path check filters, vegetation filtration, flow diversion (surface protection), armoring (surface protection), diffuser.

Example erosion and sediment controls: filter bag over sump pump hose discharge, storm drain inlet protection, flow path check filters, vegetation filtration, flow diversion (surface protection), armoring (surface protection), diffuser.

Sue Ma

(510) 622-2386

sma@waterboards.ca.gov

San Mateo County OES

400 County Center

Redwood City, CA 94063

(650) 363-4790

(650) 363-1868 fax

After hours: (650) 363-4915

Final Draft  September 2012

SMCWPPP Water Utility Work Group Fact Sheet #3